## Slide 1: An Advanced Energy Efficient Lightweight ElGamal Cryptography Technique for IoT Device
Presented By:
Regulapati Amulya and Navina K.

## Slide 2: Introduction
The importance of "An Advanced Energy Efficient Lightweight ElGamal Cryptography Technique for IoT Devices“ is as follows:
IoT Device Proliferation: With the rapid growth of IoT devices, there is a pressing need for efficient and secure communication between these devices.
Security Concerns: IoT devices often handle sensitive data and require robust cryptographic techniques to ensure data confidentiality and integrity.
ElGamal Cryptography: ElGamal is a widely used public-key cryptography technique known for its security. Adapting it for IoT devices can enhance their security.
Energy Efficiency: IoT devices are typically resource-constrained, with limited battery life. An energy-efficient cryptographic technique can significantly prolong device operation.
Lightweight Design: The lightweight design of the proposed technique is crucial for IoT devices, as it minimizes the computational and memory overhead.

## Slide 3: Introduction Contd.
Scalability: As the IoT ecosystem continues to grow, scalable cryptographic solutions become imperative. The proposed technique should be able to accommodate a large number of devices.
Data Privacy: Ensuring data privacy is a critical concern for IoT applications, as they often involve sensitive information. ElGamal cryptography can provide strong data privacy guarantees.
Interoperability: A standardized lightweight ElGamal cryptography technique can promote interoperability among IoT devices from different manufacturers.
Resilience Against Attacks: The advanced nature of the proposed technique should make IoT devices more resilient against common cryptographic attacks, enhancing overall security.
Future-Proofing: As the IoT landscape evolves, security threats become more sophisticated. Having an advanced energy-efficient cryptographic technique helps future-proof IoT devices.

## Slide 4: Introduction Contd.
Compliance: Many industries and regulatory bodies have specific security requirements. Adhering to cryptographic standards like this can help IoT devices meet compliance requirements.
Trustworthiness: Enhancing the security of IoT devices can build trust among consumers and businesses, encouraging greater adoption of IoT technology.
Reduced Operational Costs: Improved energy efficiency not only extends device lifespan but also reduces the operational costs associated with maintaining and replacing IoT devices.
Environmental Impact: Longer-lasting, energy-efficient IoT devices can have a positive impact on the environment by reducing electronic waste.
Research Advancement: Such research contributes to the field of cryptography, fostering innovation and knowledge dissemination.

## Slide 5: Motivation
- Growing importance of IoT devices in various industries and everyday life.
- Increasing demand for secure communication and data exchange in IoT.
- Current cryptographic techniques may be resource-intensive for energy-constrained IoT devices.
- Opportunity to develop a more energy-efficient cryptographic solution for IoT.
- Potential to enhance the security and longevity of IoT devices through advanced cryptography.
- Addressing the specific needs and challenges of IoT security can have a significant impact.
- Contribution to the advancement of IoT technology and its widespread adoption.
- The possibility of improving the overall efficiency and sustainability of IoT networks.
- Intellectual curiosity and interest in cryptography and its application in IoT.
- Desire to make a meaningful contribution to the field of cybersecurity and IoT.

## Slide 6: System Model
Recently, the IoT technology has become popular with the availability of low cost and efficient wireless sensors [1–3].
Nowadays, the IoT technology is used in many engineering applications [4–6].
The IoT is a typical organization comprising regular members who can recognise and communicate with similar devices over the Internet.
Cyberattacks can seriously disrupt any industrial setup if the server receives inaccurate information, leading to poor management as the outcome of the inadequate analysis.
This is a serious security problem that has to be resolved. Our research goal is to create a cryptography technique that can effectively encrypt and decrypt data being delivered across a variety of IOT devices.
This technological development offers the best plan for advancing IoT as the Internet of Everything (IoE) in the future.

## Slide 7: System Model
The complexity of IoT has also substantially increased because anything may send data to other devices online from anywhere in the world.
This extremely useful data sharing over an IoT platform must be transmitted more securely to another device.
The following are the three main causes of IoT being easily attacked by online criminals.
(a) IoT lacks a management system or an intelligent way to recognise intruders.
(b) Because IoT uses a wireless channel, spying is relatively easy.
(c) The Internet of Things accepts low computational capabilities and low energy usage

## Slide 8
A Cryptographic system for IoT

## Slide 9
The science of cracking codes for secure communication is known as cryptography.
In order to guarantee total security in IoT systems, the symmetric cryptography method, which uses the same key for both the encryption and decryption processes, must be used.
An encryption technique with little computational effort or both is known as lightweight cryptography.
Its goal is to expand the use of cryptography on limited devices, and its international standardization and compilation of guidelines are now underway.
A technical competition called CAESAR has been launched to support verified encryption that meets confidentiality and integrity requirements.
In order to pass the second round of CAESAR selection, NEC developed a compact TWINE block cypher and an authorised OTR encryption method.

## Slide 10: Literature Survey

## Slide 11
S. NO. | Name of the paper | Year | Author | Keypoints
1 | Efficient power distribution model for iot nodes driven by energy harvested from low power absent RF signal | 2019 | P prakasam, T R Suresh kumar, T velmurugan | The paper proposes a power dissemination strategy based on NASH bargaining arrangements. The goal of the strategy is to efficiently utilize nodes with the least accessibility. The paper examines available antenna technologies and suggests an optimal design to maximize energy extraction from low-power RF signals. The strategy aims to enable battery-powered sensor nodes to achieve various design objectives, including lifespan, cost-effectiveness, power sensing capabilities, transmission coverage, and consistency. The proposed technique is compared and validated against other reported methods. It is found that the proposed NASH bargaining strategy significantly improves energy efficiency, network lifetime, and throughput rate.

## Slide 12
2 | Lightweight Cryptography for Internet of Insecure Things: A Survey | 2019 | Indira Kalyan Dutta, Bhaskar Ghosh, Magdy Bayoumi | The study focuses on lightweight cryptographic methods for the Internet of Things (IoT). It covers a broad spectrum of security measures, including lightweight cryptographic techniques and a comparison of various block cipher variants. The study includes an evaluation of the Advanced Encryption Standard (AES), which is widely recognized and extensively researched. The comparison involves contemporary techniques of design, the Mix-Column/S-box modification strategy, and an assessment of IoT security threats. The study concludes that lightweight AES is effective security solution for resource-constrained IoT devices.
3 | A review on lightweight cryptography for Internet-of-Things based applications | 2021 | Rao, Vidya, and K. V. Prema | The study highlights significant security concerns related to certain protocols. These concerns revolve around the need for low computation requirements and resistance to various types of attacks, including man-in-the-middle, replay attacks, denial of service attacks, forgery, and chosen-ciphertext attacks.

## Slide 13
4 | Lightweight Cryptography Algorithms for Internet of Things enabled Networks: An Overview | 2021 | L.Mary Shamala, Dr.G.Zayarz, Dr.K.Vivekanandan, Dr.V.Vijayalakshmi | The paper discusses security risks and requirements associated with IoT (Internet of Things) cryptography. It explores the challenges and issues faced in securing IoT devices and systems. The paper includes a comparison of existing IoT security solutions to address these challenges. The study aims to provide insights into the evolving technology and trends in IoT security.
5 | Next Generation Lightweight Cryptography for Smart IoT Devices | 2020 | Nilupulee A. Gunathilake, William J. Buchanan and Rameez Asif | The paper focuses on evaluating the performance of Long-Range Wide Area Network (LoRaWAN). LoRaWAN is an open standard that defines the communication protocol for Low-Power Wide Area Network (LPWAN) technology. The paper discusses the implementation of Lightweight Cryptography (LWC) algorithms in the context of smart IoT devices. It addresses the challenges and difficulties associated with the implementation of LWC algorithms.

## Slide 14: Methodology
Data communication and data protection depend heavily on security. It helps prevent unwanted access to sensitive data that could lead to data loss or alteration by unidentified parties, making data transmission unsafe.
Following figure shows the workflow of the ElGamal algorithm. Public key cryptography is used in ElGamal encryption. For two-party communication, it encrypts the message and employs asymmetric key encryption. This cryptosystem is based on the fact that, even with knowledge of gk and ga, the discrete logarithms in the cyclic group, it is difficult to calculate gak.
If we want to understand the whole picture, we have to go step by step by actually encrypting and decrypting the messages. We will use the example of two peers willing to exchange data using the ElGamal technique securely. Consider that User–1 and User–2 wish to transmit information covertly, in which case the steps below will be performed

## Slide 15: Block Diagram

## Slide 16: Block Diagram Cond.
Step 1: Public and Private Key Generation: User–1 attempts to choose a cyclic group and a very lengthy or large integer, x. Additionally, it will choose component b and the subsequent element c from this cyclic group. The values will be selected in a way that, when the desired function is employed, the outcome equals to 1.
Step 2: User–2 encrypts the data using user1's public key: There are specific settings that User–2 must select in order to begin encrypting a message. Additionally, the User–2 will need to select one of the cyclic group's p values. A cyclic group will be utilised, similar to User–1. It is important to choose the value so that it passes through and produces a 1 in the designated function.
Step 3: Decrypt the message at user 1's end: Computing the values selected in the first and second phases, User–1 eventually determines the proper number that will be utilised to decrypt the encrypted message. User–1 processes bap and divides the result by Z to obtain the decrypted value. In the second stage, something was encrypted, and that something was the value that was decrypted. The algorithm's heart and soul are the private and public keys, which User–1 calculated to start the process in the example above. In the following stage, User–2 continues to encrypt the method using the key.

## Slide 17: Hardware Requirements
IoT Device: This is the physical hardware that you want to secure using the E3LCM encryption method. It could be a sensor, a small microcontroller, or any IoT device.
Microcontroller/Processor: The IoT device should have a microcontroller or processor capable of performing bitwise operations, multiplexing, and other cryptographic operations as required by the E3LCM algorithm.
Input/Output Pins: The microcontroller should have input and output pins to connect to the data and control bits for encryption and to communicate with other devices.
Multiplexers: You will need two-input multiplexers (Mux0 and Mux1) to implement the E3LCM algorithm. These multiplexers are used for data manipulation based on control bits.
Power Supply: Ensure that the IoT device has a reliable power supply, as encryption operations can consume energy

## Slide 18: SOFTWARE REQUIREMENTS:
E3LCM Algorithm: Develop or obtain the software implementation of the E3LCM algorithm. This includes the logic for data grouping, swapping based on control bits, and interaction with multiplexers.
Control Bit Generation
Device Firmware: Write firmware for your IoT device that integrates the E3LCM algorithm. This firmware should handle the encryption process, including receiving data, generating control bits, and applying the E3LCM algorithm.
Communication Protocols
Testing and Debugging Tools

## Slide 19: Result
This figure shows the outcome of our method and screenshots of cryptic messages.

## Slide 20: Result
The probabilistic nature of ElGamal encryption allows a single plaintext to be encrypted to a huge number of different cypher texts.
The size of the cypher text over the plaintext is therefore expanded by a factor of 2:1 as a result of a general ElGamal encryption.
Two exponentiations are essential for ElGamal encryption, but they are independent of the message and can be computed in advance if necessary.
Despite their ease of integration into a single exponentiation, decryption only needs one exponentiation and one computation of a group inverse.

## Slide 21: Comparison:
Chart: Comparison of encryption time among RSA, Elgamal and Paillier
| 68 | 105 | 124 | 235 | 435
RSA | 0.3 | 0.5 | 0.9 | 1.4 | 2.7
ElGamal | 0.9 | 1.3 | 0 | 3 | 0
Paillier | 0.2 | 0.4 | 0.9 | 2.5 | 2.8

## Slide 22: Comparison:
Public-key cryptography techniques like ElGamal, RSA, and Paillier are used for digital signatures, encryption, and decryption.
RSA: Ron Rivest, Adi Shamir, and Leonard Adleman, who created the RSA algorithm, are honoured with their names. It also takes into account how challenging factoring big numbers is. RSA is frequently used for digital signatures, encryption, and decryption. The algorithm has the advantage of being relatively fast and easy to implement.
Paillier: The Paillier algorithm is based on the difficulty of the decisional composite residuosity problem. It is a probabilistic algorithm that provides both encryption and homomorphic properties, which means that computations can be performed on cypher texts without decrypting them first. Paillier is often used in secure multiparty computation and privacy-preserving data analysis.

## Slide 23: Throughput:
Chart: 
| RSA | ElGamal | Paillier
Throughput | 0.01 | 0.11 | 0.0008
Chart: 
| RSA | ElGamal | Paillier
Throughput | 0.6 | 0.3 | 0.0008
Throughput of encryption scheme
Throughput of the decryption scheme

## Slide 24
Table represents a comparison among three algorithms. Different key values are tabulated to show the outcomes. The throughput of Elgamal Algorithm outperforms RSA and Pailler.
It performs better for the lightweight key size and validates our research. While the other two algorithms can be referred for a wide range of key sizes.

## Slide 25: Conclusion
Proposed advanced lightweight and energy-efficient ElGamal encryption method for two-party communication.
Combined asymmetric key encryption with public-key cryptography to enhance message security.
Utilized the difficulty of locating discrete logarithms in cyclic groups for cryptographic foundation.
Conducted thorough testing with text data and validation using modern cartographic techniques.
Comparative analysis revealed that the suggested strategy offers superior throughput and performance area with minimal delay.
The lightweight and highly secure ElGamal cybertext block encryption method is suitable for various secure real-time applications.
Future prospects involve further testing, evaluation, and validation across diverse real-time applications to enhance performance metrics.

## Slide 26: References:
1. Visalakshi Annepu and Rajesh A., “Implementation of an Efficient Artificial Bee Colony Algorithm for Node Localization in Unmanned Aerial Vehicle Assisted Wireless Sensor Networks”, Wireless Personal Communications, Springer, vol. 114, no. 3, pp. 2663–2680, May 2020.
2. Visalakshi Annepu and Rajesh A., “An Unmanned Aerial Vehicle Aided Node Localization Using an Efficient Multilayer Perceptron Neural Network in Wireless Sensor Networks”, Neural Computing and Applications, Springer, vol. 32, no. 15, pp. 11651–11663, August 2020.
3. V. Annepu, A. Rajesh and K. Bagadi, “Radial basis function-based node localization for unmanned aerial vehicle-assisted 5G wireless sensor networks”, Neural Computing and Applications, 33, 12333-12346, 2021.
4. V. Annepu et al., "Review on Unmanned Aerial Vehicle Assisted Sensor Node Localization in Wireless Networks: Soft Computing Approaches," IEEE Access, vol. 10, pp. 132875-132894, 2022
5. N. K. Vaegae, K. K. Pulluri, K. Bagadi and O. O. Oyerinde, "Design of an Efficient Distracted Driver Detection System: Deep Learning Approaches," IEEE Access, vol. 10, pp. 116087-116097, November 2022.

## Slide 27: References:
6. K. Bagadi, C. V. Ravikumar, M. Alibakhshikenari, Ch. Nagaraj, A. Rajesh, S. Aïssa, I. Dayoub, F. Falcone and E. Limiti, “Precoded Large Scale Multi-User-MIMO System Using Likelihood Ascent Search for Signal Detection”, Radio Science, vol. 57, no. 12, December 2022.
7. Goyal, Tarun Kumar, Vineet Sahula, and Deepak Kumawat. "Energy efficient lightweight cryptography algorithms for IoT devices." IETE Journal of Research 68, no. 3 (2022): 1722-1735.
8. Thakor, Vishal A., Mohammad Abdur Razzaque, and Muhammad RA Khandaker. "Lightweight cryptography algorithms for resource-constrained IoT devices: A review, comparison and research opportunities." IEEE Access 9 (2021): 28177-28193.
9. Dutta, Indira Kalyan, Bhaskar Ghosh, and Magdy Bayoumi. "Lightweight cryptography for internet of insecure things: A survey." In 2019 IEEE 9th Annual Computing and Communication Workshop and Conference (CCWC), pp. 0475-0481. IEEE, 2019.
10. Okello, Wanican Julian, Qingling Liu, Faizan Ali Siddiqui, and Chaozhu Zhang. "A survey of the current state of lightweight cryptography for the Internet of things." In 2017 International Conference on Computer, Information and Telecommunication Systems (CITS), pp. 292-296. IEEE, 2017.